## Slide 1
ESP8266 WORKSHOP
Exploring how NodeMCU is use to become IoT

## Slide 2
WHAT IS INTERNET of THINGS?
Network of interrelated devices that connect and exchange data with other IoT devices and the cloud.
IoT are typically embedded with technology such as sensors and software.
Network of interrelated devices that connect and exchange data with other IoT devices and the cloud.

## Slide 4
MAKING THE NodeMCU AS IoT

## Slide 5
WE NEED 4 STEPS
TO ACHIEVE OUR MISSION...
1.Toggling the on-board LED of NodeMCU.
2.Connect the NodeMCU to WiFi.
3.Making the NodeMCU as an access point.
4.Connect the NodeMCU to the Firebase.

## Slide 6
Today’s Focus
  ESP8266
  FireBase
  Internet of Things (IoT)

## Slide 7
  NodeMCU ESP8266 is a low cost open source firmware.
  Specifically used for IoT applications.
  WiFi enabled microcontroller board.
WHAT IS NODEMCU ESP8266 ?

## Slide 8
WHAT IS NODEMCU ESP8266 ?
WHAT IS NODEMCU ESP8266 ?

## Slide 9
IP4

## Slide 10
SETTING UP ESP8266 TO ARDUINO IDE

## Slide 11
1
2
Go to File > Preference
In Additional Board Manager URLs, insert this link (https://arduino.esp8266.com/stable/package_esp8266com_index.json)

## Slide 12
3
Go to Tools > Board >Board Manager
Search for esp8226 by ESP8266 Community and Install
4
Go to Tools > Board > esp8266 > NodeMCU 1.0 (ESP-12E Module)

## Slide 13
SETTING UP FIREBASE WITH IDE

## Slide 14
1
Download zip file from : https://github.com/mobizt/Firebase-ESP8266?

## Slide 15
2
Go to Sketch > Include Library > Add .ZIP file

## Slide 16
SETTING UP FIREBASE CONSOLE

## Slide 17
WHAT IS FIREBASE ?

## Slide 18
1
Go to Firebase console on google > create account
2
Once you’ve created an account, Click on Add Project.
3
Create a name for your project.
4
Enable the google analytics button and continue

## Slide 19
5
6
Setup or choose a Google Analytics account then press continue.
Go to Build > Realtime Database > Create Database
7
In set up database > database options: choose the nearest location for the realtime database. Then, press next.

## Slide 20
8
9
In set up database > security rules > choose the start in locked mode and clicked enable.
In rules, change the code from false to true. Then click Publish.

## Slide 21
STEP 1:
Toggling the on-board LED of NodeMCU.
COMPONENT
ESP8266
BreadBoard
https://github.com/idham1432/nodemcu_workshop/blob/main/step-01/LED_connect.ino
Github link:

## Slide 22
STEP 2:
Connect the NodeMCU to WiFi.
https://github.com/idham1432/nodemcu_workshop/blob/main/step-02/connect_home_internet.ino
Github link:

## Slide 23
STEP 3:
Making the NodeMCU as an access point.
1
2
3
https://github.com/idham1432/nodemcu_workshop/blob/main/step-03/accesspoint_fixIP.ino
Github link:

## Slide 24
STEP 3:
Making the NodeMCU as an access point.
4
5
https://github.com/idham1432/nodemcu_workshop/blob/main/step-03/change_pass.ino
Github link:

## Slide 25
STEP 3:
Making the NodeMCU as an access point.
6
7

## Slide 26
STEP 4:
Connect the NodeMCU to the Firebase
https://github.com/idham1432/nodemcu_workshop/blob/main/step-04/connect_to_firebase.ino
Github link:

## Slide 27
STEP 4:
Connect the NodeMCU to the Firebase

## Slide 28
STEP 4:
Connect the NodeMCU to the Firebase
Must be the same as your firebase collection

## Slide 29
STEP 4:
Connect the NodeMCU to the Firebase
https://github.com/idham1432/nodemcu_workshop/blob/main/step-04/final_test.ino
Github link:

## Slide 30
STEP 4:
Connect the NodeMCU to the Firebase

## Slide 31
STEP 4:
Connect the NodeMCU to the Firebase

## Slide 32
CREATING AN APP IN FIREBASE
Go to project overview > Your Apps > choose “</>”

## Slide 33
CREATING AN APP IN FIREBASE
  In step 2: Choose the “Use <script> tag.
  Copy the firebase configuration and paste it inside your html <script> tag.

## Slide 34
CREATING A WEB PAGE FOR UI
remember your <script> tag? copy and paste it here!

## Slide 35
CREATING A WEB PAGE FOR UI
FUNCTIONS INSIDE HTML FILE:
1
2
3
https://github.com/idham1432/nodemcu_workshop/blob/main/FIREBASE_CREDENTIAL.html
Github link:

## Slide 36
Now.. MAKE YOUR HTML PAGE TO BE USER FRIENDLY!
HINT: You need to add button for the toggle LED inside your <body> tag!

## Slide 37
Firebase link : https://trialmcu-b109a-default-rtdb.asia-southeast1.firebasedatabase.app/
auth key : UXeUN4Swyqc6W0dQlPmf8TopG6kT3zczD99nrsg0
Link library : https://github.com/links2004/arduinowebsockets/tree/master